## Slide 1
Design & Simulation of an Automatic Street Light Control System
Using Pure Combinational Logic in Logisim

## Slide 2
AUTOMATIC STREET LIGHT CONTROL
Introduction & Real-World Problem Statement
The Inefficiency Challenge
• Manual street light systems suffer from human delays and errors.
• Streetlights remain fully powered during bright daylight or low-traffic midnights.
• Massive grid power wastage and inflated municipal electricity expenses.
• Shortened bulb lifespans due to continuous unneeded burning.
The Combinational Solution
• An automated system responding dynamically to environmental variables.
• Relies completely on combinational logic for instant, memoryless operations.
• Processes sensor inputs (Light, Motion, Emergency Override) in real-time.
• Delivers substantial energy savings by adjusting brightness levels seamlessly.

## Slide 3
AUTOMATIC STREET LIGHT CONTROL
System Specifications & Variable Declarations
Variable | Type | Logic Definition
L (Light) | Input | 1 = It is Dark / Night ¦ 0 = It is Bright / Day
M (Motion) | Input | 1 = Vehicle/Pedestrian detected ¦ 0 = Idle street
E (Emerg) | Input | 1 = Override active (Fog/Repair) ¦ 0 = Normal
B1, B0 | Output | 2-bit output: 00=Off ¦ 01=Dim (30%) ¦ 10=Full (100%)
Design Requirements & Rules
✔ Rule 1: If Emergency (E=1) is active, system outputs Full Brightness (10) regardless of light or motion.
✔ Rule 2: During Day (L=0), lights remain Off (00) unless an emergency override is triggered.
✔ Rule 3: During Night (L=1) with no motion (M=0), lights stay Dim (01) to save standby energy.
✔ Rule 4: During Night (L=1) with motion (M=1), lights scale up instantly to Full Brightness (10).
E | L | M | B1 | B0 | System Operating State
0 | 0 | 0 | 0 | 0 | Daytime - Empty Street (OFF)
0 | 0 | 1 | 0 | 0 | Daytime - Motion Detected (OFF)
0 | 1 | 0 | 0 | 1 | Nighttime - Empty Street (DIM)
0 | 1 | 1 | 1 | 0 | Nighttime - Motion Detected (FULL)
1 | 0 | 0 | 1 | 0 | Emergency Override Active (FULL)
1 | 0 | 1 | 1 | 0 | Emergency Override Active (FULL)
1 | 1 | 0 | 1 | 0 | Emergency Override Active (FULL)
1 | 1 | 1 | 1 | 0 | Emergency Override Active (FULL)

## Slide 4
AUTOMATIC STREET LIGHT CONTROL
System Truth Table Derivation
Truth Table Observations
• B1 is active (1) in five specific conditions: when night motion happens or whenever emergency mode triggers.
• B0 is active (1) in only one distinct state: when it is night and there is absolutely no traffic motion.
• This deterministic mapping forms the foundation for deriving logic equations using K-Maps.

## Slide 5
AUTOMATIC STREET LIGHT CONTROL
Boolean Simplification Using K-Maps
Deriving Output B1 (MSB)
Minterms: Σm(3, 4, 5, 6, 7)
K-Map Grouping Details: - A large 4-cell grouping maps out the rows where Emergency E = 1. - A separate 2-cell vertical group maps out the intersection where L = 1 and M = 1.
Simplified Equation: B1 = E + (L · M)
Deriving Output B0 (LSB)
Minterms: Σm(2)
K-Map Grouping Details: - Only minterm m2 (010) is active for this output bit. - Cannot be grouped with any adjacent cells due to surrounding zeros. - Must be implemented as a single 3-input AND gate sequence.
Simplified Equation: B0 = E' · L · M'

## Slide 6
AUTOMATIC STREET LIGHT CONTROL
Complete Logisim Circuit Schematic
Logisim Functional Gate Architecture
INPUT PINS LOGIC GATES CONSTRUCT OUTPUT PINS ========== ==================== =========== E (Emergency) ────────┬───────────────────────────────────────────► [ B1 (MSB) ] │ ▲ │ ┌───────────┐ │ L (Light) ────┬───┼──►│ AND Gate │───────────────┘ (OR Gate) │ │ └───────────┘ M (Motion) ──┬─┼───┘ │ │ ┌───────────┐ │ └──[NOT]►│ │ └────[NOT]►│ 3-In AND ├──────────────────────────► [ B0 (LSB) ] └───────────┘
Circuit Component Inventory: 2 NOT Gates, 1 Two-Input AND Gate, 1 Three-Input AND Gate, 1 Two-Input OR Gate, 3 Input Pins, 2 Output Pins.

## Slide 7
AUTOMATIC STREET LIGHT CONTROL
Logisim Simulation: Day Mode States (OFF)
Condition: Sunlight Available (L = 0, E = 0)
➔ State [000] - Day & No Motion: Light Input is 0. Motion Input is 0. Both output bits evaluate to 0 (B1B0 = 00). Street lights remain fully Powered Down.
➔ State [001] - Day & Motion Detected: Even when a vehicle passes by (M = 1), the AND gate evaluating (L · M) receives a 0 from the light sensor. The output stays firmly at 00.
➔ Logisim Behavior: Output pins show dark green traces, indicating logic low (0 state) across both terminal paths.

## Slide 8
AUTOMATIC STREET LIGHT CONTROL
Logisim Simulation: Night Mode Dynamics
Dynamic Adjustments Under Darkness (L = 1, E = 0)
➔ State [010] - Night & Empty Street (Standby Dim): L=1 and M=0. The 3-input AND gate satisfies E'=1, L=1, M'=1. B0 switches to 1, while B1 remains 0. System outputs 01 (Dim Mode, 30% power).
➔ State [011] - Night & Active Traffic (Full Power): A vehicle triggers M=1. The sub-gate (L · M) becomes 1, propagating through the OR gate to drive B1 to 1. Simultaneously, M=1 breaks the 3-input AND condition, dropping B0 to 0. System outputs 10 (Full Power, 100% brightness).
➔ Logisim Behavior: Instantly toggles between output pins B0 and B1, dynamically moving bright green logic high wires as motion inputs change.

## Slide 9
AUTOMATIC STREET LIGHT CONTROL
Logisim Simulation: Emergency Override Mode
Condition: Override Signal Active (E = 1)
➔ Absolute Priority: When E=1 is injected, it bypasses light and motion sensor states entirely via the final output OR gate.
➔ Output Combination: B1 is driven to 1 immediately through the direct connection from E. B0 is forced to 0 because E'=0 kills the 3-input AND gate condition.
➔ System Output: B1B0 = 10 (Full 100% Brightness) across all binary variations of L and M (States 100, 101, 110, 111).
➔ Use Cases: Vital for safety during hazardous heavy fog, unexpected solar eclipses, road maintenance work, or physical manual logic testing overrides.

## Slide 10
Project Summary & Energy Advantages
✔ Validated Design: A fully functional, real-time reactive street light model built strictly using primitive logic gates.
✔ Power Preservation: Slashing power draw by 70% during inactive night hours by utilizing the smart 01 (Dim) state.
✔ Purely Combinational: Instant structural response with zero clock cycles, zero software delay overhead, and zero volatile memory dependencies.
✔ Scalability: Ready for real-world hardware deployment using standard 74xx series discrete ICs (7404, 7408, 7432) or simple PLD architectures.